## Slide 1
Using Automation to Provide High-Quality
Analytical Data in Drug Checking and Point of Care Services
Clark Zhang1, Matthew E. Reish1, Rebekah Greenwood1, Guy Swain1, Rebecca Hickman1, Sara Guzman1 and Jason E. Hein1-3
Affiliations
Department of Chemistry, The University of British Columbia, 2036 Main Mall, Vancouver
Acceleration Consortium, University of Toronto, 700 University Ave suite 1001, Toronto
Department of Chemistry, University of Bergen, Allégaten 41, 5007 Bergen, Norway
Each year, there are over 10,000 cases of overdose in Vancouver1, many due to drug contamination. In response to the current overdose health crisis, numerous drug-checking centers have been set up, often using test strips to identify compounds and infrared spectroscopy for quantification. Despite governmental efforts, access to advanced methods like high-performance liquid chromatography (HPLC) remains limited. As operations of these technologies require specialized personnel, we can improve accessibility to these systems by integrating automation.
We are developing a robotic arm system to prepare, analyze, quantify, and upload the data of a sample within 15 minutes to inform users, ultimately reducing overdose risk.
Scan the QR code
for an annotated
demonstration video
A Deeper Look
All functions required for operation are coded in Python. Relevant code can be found on the Hein Lab GitHub.
Software
Calibration curves were autonomously generated by the robot. Shown below are the curves for caffeine and acetaminophen.
Design Verification
Chart: Analyte Concentration (mg/mL)
| 0 | 7.1298381044280044 | 3.2742491383554899 | 3.8085797676083484 | 5.9160411453989443 | 7.9556127012522371 | 7.3727532336636994 | 10.427492274236007 | 10.443030719853278 | 9.608715755403999 | 13.200746268656717 | 14.060133239831698 | 14.925284980213808 | 16.63677130044843 | 18.408028759736375 | 17.472063854047892
 | 0 | 1.401 | 0.81238 | 0.75367 | 1.174 | 1.5504 | 1.4546 | 1.9575 | 2.0506 | 1.9451 | 2.5694 | 2.8388 | 3.0445 | 3.3017 | 3.7099 | 3.6515
Caffeine calibration curve
Chart: Analyte Concentration (mg/mL)
| 0 | 0.3974652401572058 | 0.30842652646231355 | 0.25364818297972019 | 0.21908936855126449 | 0.19490053720633824 | 0.17177626347154459 | 0.1520710487076935 | 0.13001493339887957 | 0.12423983616904498 | 1.2954171447383274 | 0.91173250328070532 | 0.71412026572940079 | 0.56687595501996313 | 0.46441700562084742 | 0.37179306074309004 | 0.52618416967649473 | 0.72736601507756293 | 0.64642143951412223 | 0.55321223214653548 | 0.43739052203366502 | 0.28842754921415309 | 8.8733818223640556E-2 | 0.38978351180899329 | 0.4685543389116168 | 0.53892713109336299 | 0.61359167954627125 | 0.68085129590278459 | 0.70290448682716467 | 0.81386676191372309 | 0.95588073680616092
 | 0 | 336.9667 | 255.5186 | 211.9316 | 189.2519 | 156.0314 | 136.9568 | 123.1748 | 110.3618 | 106.2606 | 1093.9274 | 757.6731 | 589.7725 | 455.2367 | 412.7721 | 305.1734 | 432.8267 | 625.36 | 525.9481 | 451.493 | 348.5228 | 226.3438 | 71.545 | 311 | 422.22 | 464.6054 | 508.1615 | 562.1576 | 569.85 | 824.3738
Acetaminophen calibration curve
In the next phase of our project, we will expand our analytical library to include a wider range of substances, including methamphetamine, heroin, cocaine, and fentanyl.
Additionally, we will develop a program to automatically upload results to our website where individuals can access their analysis data by entering their vial ID. This feature will provide timely and accurate information, further enhancing the safety and awareness of drug users.
Future Work
UR3e robot with grippers to operate vial transfers between components
3/8” aluminum platform with machined M4 holes
Liquid Handler made with chemical-resistant plastic designed to precisely dispense and aspirate samples
3D-printed vial trays designed to house 15 HPLC vials and centrifuge vials
2
3D-printed housing for a stepper motor-activated Fisher vortexer
3
4
Agilent HPLC for substance analysis
8
Barcode reader designed with a Razer webcam and 3D-printed mount
6
1
Mettler-Toledo balance mounted underneath platform using 3D-printed legs
7
9
Hidden Components
3D-printed electronics box to house stepper motor and BLDC motor controllers
Syringe pump and solvent and waste bottle housing behind the HPLC
User input required
Vial tared and barcode applied
Vial is loaded with solid sample
Vial loaded into
vial tray
Dilute sample
with solute
Prime needle
Scan and
weigh vial
Vortex and centrifuge
Transfer stock solution to
HPLC vial and dilute
Run sample through HPLC
Pre-run
Sample Preparation
Extract relevant area data
Correlate to mass % using calibration curve
Upload data
Analysis
67.5 cm
References
BC Emergency Health Services, http://www.bcehs.ca, 2023
Custom BLDC motor centrifuge operated by an O-Drive motor controller spinning at a maximum of 12000 rpm.
5

## Slide 2
Using Automation to Provide High-Quality
Analytical Data in Drug Checking and Point of Care Services
Clark Zhang1, Matthew E. Reish1, Rebekah Greenwood1, Guy Swain1, Rebecca Hickman1, Sara Guzman1 and Jason E. Hein1-3
Affiliations
Department of Chemistry, The University of British Columbia, 2036 Main Mall, Vancouver
Acceleration Consortium, University of Toronto, 700 University Ave suite 1001, Toronto
Department of Chemistry, University of Bergen, Allégaten 41, 5007 Bergen, Norway
Each year, there are over 10,000 cases of overdose in Vancouver1, many due to drug contamination. In response to the current overdose health crisis, numerous drug-checking centers have been set up, often using test strips to identify compounds and infrared spectroscopy for quantification. Despite governmental efforts, access to advanced methods like high-performance liquid chromatography (HPLC) remains limited. As operations of these technologies require specialized personnel, we can improve accessibility to these systems by integrating automation.
We are developing a robotic arm system to prepare, analyze, quantify, and upload the data of a sample within 15 minutes to inform users, ultimately reducing overdose risk.
Scan the QR code
for an annotated
demonstration video
A Deeper Look
All functions required for operation are coded in Python. Relevant code can be found on the Hein Lab GitHub.
Software
Calibration curves were autonomously generated by the robot. Shown below are the curves for caffeine and acetaminophen.
Design Verification
Chart: Analyte Concentration (mg/mL)
| 0 | 7.1298381044280044 | 3.2742491383554899 | 3.8085797676083484 | 5.9160411453989443 | 7.9556127012522371 | 7.3727532336636994 | 10.427492274236007 | 10.443030719853278 | 9.608715755403999 | 13.200746268656717 | 14.060133239831698 | 14.925284980213808 | 16.63677130044843 | 18.408028759736375 | 17.472063854047892
 | 0 | 1.401 | 0.81238 | 0.75367 | 1.174 | 1.5504 | 1.4546 | 1.9575 | 2.0506 | 1.9451 | 2.5694 | 2.8388 | 3.0445 | 3.3017 | 3.7099 | 3.6515
Caffeine calibration curve
Chart: Analyte Concentration (mg/mL)
| 0 | 0.3974652401572058 | 0.30842652646231355 | 0.25364818297972019 | 0.21908936855126449 | 0.19490053720633824 | 0.17177626347154459 | 0.1520710487076935 | 0.13001493339887957 | 0.12423983616904498 | 1.2954171447383274 | 0.91173250328070532 | 0.71412026572940079 | 0.56687595501996313 | 0.46441700562084742 | 0.37179306074309004 | 0.52618416967649473 | 0.72736601507756293 | 0.64642143951412223 | 0.55321223214653548 | 0.43739052203366502 | 0.28842754921415309 | 8.8733818223640556E-2 | 0.38978351180899329 | 0.4685543389116168 | 0.53892713109336299 | 0.61359167954627125 | 0.68085129590278459 | 0.70290448682716467 | 0.81386676191372309 | 0.95588073680616092
 | 0 | 336.9667 | 255.5186 | 211.9316 | 189.2519 | 156.0314 | 136.9568 | 123.1748 | 110.3618 | 106.2606 | 1093.9274 | 757.6731 | 589.7725 | 455.2367 | 412.7721 | 305.1734 | 432.8267 | 625.36 | 525.9481 | 451.493 | 348.5228 | 226.3438 | 71.545 | 311 | 422.22 | 464.6054 | 508.1615 | 562.1576 | 569.85 | 824.3738
Acetaminophen calibration curve
In the next phase of our project, we will expand our analytical library to include a wider range of substances, including methamphetamine, heroin, cocaine, and fentanyl.
Additionally, we will develop a program to automatically upload results to our website where individuals can access their analysis data by entering their vial ID. This feature will provide timely and accurate information, further enhancing the safety and awareness of drug users.
Future Work
UR3e robot with grippers to operate vial transfers between components
3/8” aluminum platform with machined M4 holes
Custom BLDC motor centrifuge operated by an O-Drive motor controller spinning at a maximum of 12000 rpm.
Needle wash station made with chemical-resistant plastic designed to clean the needle between runs
5
3D-printed vial trays designed to house 15 HPLC vials and centrifuge vials
2
3D-printed housing for a stepper motor-activated Fisher vortexer
3
4
Agilent HPLC for substance analysis
8
Barcode reader designed with a Razer webcam and 3D-printed mount
6
1
Mettler-Toledo balance mounted underneath platform using 3D-printed legs
7
9
Hidden Components
3D-printed electronics box to house stepper motor and BLDC motor controllers
Syringe pump and solvent and waste bottle housing behind the HPLC
User input required
Vial tared and barcode applied
Vial is loaded with solid sample
Vial loaded into
vial tray
Dilute sample
with solute
Prime needle
Scan and
weigh vial
Vortex and centrifuge
Transfer stock solution to
HPLC vial and dilute
Run sample through HPLC
Pre-run
Sample Preparation
Extract relevant area data
Correlate to mass % using calibration curve
Upload data
Analysis
67.5 cm
References
BC Emergency Health Services, http://www.bcehs.ca, 2023